## Slide 1
Fit plugs flush to surface and lightly thread lock into place

## Slide 2
Mount with 8x
M5x45mm cap head screw
Orient load cell to direct cable near parallel to straight edges of mounting plate
Plugs should face each other

## Slide 3
50kg load cell mounted between two thread adaptors – tighten by hand only. Ideally use shake proof split washers.

## Slide 4
Mount centring ring with 2x M4x25mm countersunk head screws
Mount alignment and associated cap plate with 3x M8x40mm cap head screws

## Slide 5
Closest approach at 160mm travel: stud length ensures clash should not occur with clamp (given clamp orientation shown)
Stud and right hand nut lightly thread locked into clamp body

## Slide 6
Stud lightly thread locked into compression plate body and last nut lightly thread locked into place
Stud length and nut stack ensures clash should not occur with compression plate

## Slide 7
Stud lightly thread locked into clamp body

## Slide 8
Stud lightly thread locked into compression plate body